Lab VLAN
Redes II, TUASySL
pc1:~# ping -c 3 pc2 / PING pc2 (192.168.0.2) 56(84) bytes of data. / 64 bytes from pc2 (192.168.0.2): icmp_seq=1 ttl=63 time=14.3 ms / 64 bytes from pc2 (192.168.0.2): icmp_seq=2 ttl=63 time=2.38 ms / 64 bytes from pc2 (192.168.0.2): icmp_seq=3 ttl=63 time=1.65 ms / --- pc2 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2006ms / rtt min/avg/max/mdev = 1.652/6.127/14.344/5.818 ms / pc1:~# / pc1:~# ping -c 3 pc3 / PING pc3 (192.168.0.3) 56(84) bytes of data. / 64 bytes from pc3 (192.168.0.3): icmp_seq=1 ttl=63 time=8.09 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=2 ttl=63 time=0.345 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=3 ttl=63 time=1.75 ms / --- pc3 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2007ms / rtt min/avg/max/mdev = 0.345/3.399/8.093/3.368 ms / pc1:~# / pc1:~# ping -c 3 pc4 / PING pc4 (10.0.0.3) 56(84) bytes of data. / 64 bytes from pc4 (10.0.0.3): icmp_seq=1 ttl=64 time=10.8 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=2 ttl=64 time=1.91 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=3 ttl=64 time=1.03 ms / --- pc4 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2005ms / rtt min/avg/max/mdev = 1.038/4.586/10.806/4.413 ms / pc1:~# / pc1:~# ping -c 3 r1 / PING r1 (10.0.0.1) 56(84) bytes of data. / 64 bytes from r1 (10.0.0.1): icmp_seq=1 ttl=64 time=0.242 ms / 64 bytes from r1 (10.0.0.1): icmp_seq=2 ttl=64 time=1.10 ms / 64 bytes from r1 (10.0.0.1): icmp_seq=3 ttl=64 time=0.656 ms / --- r1 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2007ms / rtt min/avg/max/mdev = 0.242/0.668/1.107/0.353 ms / pc1:~#
pc2:~# ping -c 3 pc1 / PING pc1 (10.0.0.2) 56(84) bytes of data. / 64 bytes from pc1 (10.0.0.2): icmp_seq=1 ttl=63 time=16.9 ms / 64 bytes from pc1 (10.0.0.2): icmp_seq=2 ttl=63 time=2.09 ms / 64 bytes from pc1 (10.0.0.2): icmp_seq=3 ttl=63 time=0.373 ms / --- pc1 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2002ms / rtt min/avg/max/mdev = 0.373/6.462/16.916/7.425 ms / pc2:~# / pc2:~# ping -c 3 pc3 / PING pc3 (192.168.0.3) 56(84) bytes of data. / 64 bytes from pc3 (192.168.0.3): icmp_seq=1 ttl=64 time=10.6 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=2 ttl=64 time=1.09 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=3 ttl=64 time=0.505 ms / --- pc3 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 1998ms / rtt min/avg/max/mdev = 0.505/4.072/10.614/4.632 ms / pc2:~# / pc2:~# ping -c 3 pc4 / PING pc4 (10.0.0.3) 56(84) bytes of data. / 64 bytes from pc4 (10.0.0.3): icmp_seq=1 ttl=63 time=7.50 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=2 ttl=63 time=2.04 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=3 ttl=63 time=1.93 ms / --- pc4 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2009ms / rtt min/avg/max/mdev = 1.937/3.828/7.503/2.599 ms / pc2:~# / pc2:~# ping -c 3 r1 / PING r1 (192.168.0.1) 56(84) bytes of data. / 64 bytes from r1 (192.168.0.1): icmp_seq=1 ttl=64 time=0.191 ms / 64 bytes from r1 (192.168.0.1): icmp_seq=2 ttl=64 time=0.225 ms / 64 bytes from r1 (192.168.0.1): icmp_seq=3 ttl=64 time=0.299 ms / --- r1 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 1998ms / rtt min/avg/max/mdev = 0.191/0.238/0.299/0.046 ms / pc2:~#
pc3:~# ping -c 3 pc1 / PING pc1 (10.0.0.2) 56(84) bytes of data. / 64 bytes from pc1 (10.0.0.2): icmp_seq=1 ttl=63 time=10.5 ms / 64 bytes from pc1 (10.0.0.2): icmp_seq=2 ttl=63 time=0.871 ms / 64 bytes from pc1 (10.0.0.2): icmp_seq=3 ttl=63 time=1.74 ms / --- pc1 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 1999ms / rtt min/avg/max/mdev = 0.871/4.399/10.581/4.386 ms / pc3:~# / pc3:~# ping -c 3 pc2 / PING pc2 (192.168.0.2) 56(84) bytes of data. / 64 bytes from pc2 (192.168.0.2): icmp_seq=1 ttl=64 time=10.5 ms / 64 bytes from pc2 (192.168.0.2): icmp_seq=2 ttl=64 time=1.08 ms / 64 bytes from pc2 (192.168.0.2): icmp_seq=3 ttl=64 time=1.14 ms / --- pc2 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 1998ms / rtt min/avg/max/mdev = 1.088/4.269/10.579/4.461 ms / pc3:~# / pc3:~# ping -c 3 pc4 / PING pc4 (10.0.0.3) 56(84) bytes of data. / 64 bytes from pc4 (10.0.0.3): icmp_seq=1 ttl=63 time=0.534 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=2 ttl=63 time=2.00 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=3 ttl=63 time=2.41 ms / --- pc4 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2011ms / rtt min/avg/max/mdev = 0.534/1.651/2.416/0.807 ms / pc3:~# / pc3:~# ping -c 3 r1 / PING r1 (192.168.0.1) 56(84) bytes of data. / 64 bytes from r1 (192.168.0.1): icmp_seq=1 ttl=64 time=0.314 ms / 64 bytes from r1 (192.168.0.1): icmp_seq=2 ttl=64 time=1.37 ms / 64 bytes from r1 (192.168.0.1): icmp_seq=3 ttl=64 time=0.845 ms / --- r1 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2007ms / rtt min/avg/max/mdev = 0.314/0.844/1.374/0.433 ms / pc3:~#
pc4:~# ping -c 3 pc1 / PING pc1 (10.0.0.2) 56(84) bytes of data. / 64 bytes from pc1 (10.0.0.2): icmp_seq=1 ttl=64 time=5.28 ms / 64 bytes from pc1 (10.0.0.2): icmp_seq=2 ttl=64 time=1.43 ms / 64 bytes from pc1 (10.0.0.2): icmp_seq=3 ttl=64 time=1.00 ms / --- pc1 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2005ms / rtt min/avg/max/mdev = 1.005/2.574/5.285/1.925 ms / pc4:~# / pc4:~# ping -c 3 pc2 / PING pc2 (192.168.0.2) 56(84) bytes of data. / 64 bytes from pc2 (192.168.0.2): icmp_seq=1 ttl=63 time=8.16 ms / 64 bytes from pc2 (192.168.0.2): icmp_seq=2 ttl=63 time=0.741 ms / 64 bytes from pc2 (192.168.0.2): icmp_seq=3 ttl=63 time=0.834 ms / --- pc2 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 1998ms / rtt min/avg/max/mdev = 0.741/3.247/8.166/3.478 ms / pc4:~# / pc4:~# ping -c 3 pc3 / PING pc3 (192.168.0.3) 56(84) bytes of data. / 64 bytes from pc3 (192.168.0.3): icmp_seq=1 ttl=63 time=0.496 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=2 ttl=63 time=0.537 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=3 ttl=63 time=0.665 ms / --- pc3 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 1998ms / rtt min/avg/max/mdev = 0.496/0.566/0.665/0.071 ms / pc4:~# / pc4:~# ping -c 3 r1 / PING r1 (10.0.0.1) 56(84) bytes of data. / 64 bytes from r1 (10.0.0.1): icmp_seq=1 ttl=64 time=0.316 ms / 64 bytes from r1 (10.0.0.1): icmp_seq=2 ttl=64 time=1.08 ms / 64 bytes from r1 (10.0.0.1): icmp_seq=3 ttl=64 time=0.489 ms / --- r1 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2007ms / rtt min/avg/max/mdev = 0.316/0.629/1.083/0.329 ms / pc4:~#
r1:~# ping -c 3 pc1 / PING pc1 (10.0.0.2) 56(84) bytes of data. / 64 bytes from pc1 (10.0.0.2): icmp_seq=1 ttl=64 time=0.207 ms / 64 bytes from pc1 (10.0.0.2): icmp_seq=2 ttl=64 time=1.04 ms / 64 bytes from pc1 (10.0.0.2): icmp_seq=3 ttl=64 time=0.918 ms / --- pc1 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2011ms / rtt min/avg/max/mdev = 0.207/0.723/1.046/0.370 ms / r1:~# / r1:~# ping -c 3 pc2 / PING pc2 (192.168.0.2) 56(84) bytes of data. / 64 bytes from pc2 (192.168.0.2): icmp_seq=1 ttl=64 time=0.218 ms / 64 bytes from pc2 (192.168.0.2): icmp_seq=2 ttl=64 time=0.675 ms / 64 bytes from pc2 (192.168.0.2): icmp_seq=3 ttl=64 time=1.03 ms / --- pc2 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2007ms / rtt min/avg/max/mdev = 0.218/0.641/1.031/0.333 ms / r1:~# / r1:~# ping -c 3 pc3 / PING pc3 (192.168.0.3) 56(84) bytes of data. / 64 bytes from pc3 (192.168.0.3): icmp_seq=1 ttl=64 time=0.306 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=2 ttl=64 time=1.46 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=3 ttl=64 time=1.21 ms / --- pc3 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2006ms / rtt min/avg/max/mdev = 0.306/0.994/1.465/0.497 ms / r1:~# / r1:~# ping -c 3 pc4 / PING pc4 (10.0.0.3) 56(84) bytes of data. / 64 bytes from pc4 (10.0.0.3): icmp_seq=1 ttl=64 time=0.283 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=2 ttl=64 time=1.38 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=3 ttl=64 time=0.847 ms / --- pc4 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2006ms / rtt min/avg/max/mdev = 0.283/0.838/1.385/0.450 ms / r1:~#

variamos las cache arp
r1:~# ip -s -s neigh flush all / 192.168.0.3 dev eth0.20 lladdr 00:00:00:00:00:03 ref 4 used 111/111/82 STALE / 192.168.0.2 dev eth0.20 lladdr 00:00:00:00:00:02 ref 4 used 135/135/107 STALE / 10.0.0.3 dev eth0.10 lladdr 00:00:00:00:00:04 ref 4 used 90/90/70 STALE / 10.0.0.2 dev eth0.10 lladdr 00:00:00:00:00:01 ref 4 used 145/145/125 STALE / *** Round 1, deleting 4 entries *** / *** Flush is complete after 1 round *** / r1:~# / pc1:~# ip -s -s neigh flush all / 10.0.0.3 dev eth0 lladdr 00:00:00:00:00:04 ref 1 used 236/236/197 STALE / 10.0.0.1 dev eth0 lladdr 00:00:00:00:00:0a ref 2 used 153/153/114 STALE / *** Round 1, deleting 2 entries *** / *** Flush is complete after 1 round *** / pc1:~# / pc4:~# ip -s -s neigh flush all / 10.0.0.2 dev eth0 lladdr 00:00:00:00:00:01 ref 2 used 240/240/223 STALE / 10.0.0.1 dev eth0 lladdr 00:00:00:00:00:0a ref 6 used 104/104/73 STALE / *** Round 1, deleting 2 entries *** / *** Flush is complete after 1 round *** / pc4:~#

 iniciamos los monitores en segundo plano

r1:~# tcpdump -s 0 -w /hostlab/r1.cap & / [1] 814 / r1:~# tcpdump: WARNING: eth0: no IPv4 address assigned / tcpdump: listening on eth0, link-type EN10MB (Ethernet), capture size 65535 bytes / job / -bash: job: command not found / r1:~# jobs / [1]+ Running tcpdump -s 0 -w /hostlab/r1.cap & / r1:~#
pc2:~# tcpdump -s 0 -w /hostlab/pc2.cap & / [1] 1649 / pc2:~# tcpdump: listening on eth0, link-type EN10MB (Ethernet), capture size 65535 bytes / jobs / [1]+ Running tcpdump -s 0 -w /hostlab/pc2.cap & / pc2:~#
pc4:~# tcpdump -s 0 -w /hostlab/pc4.cap & / [1] 815 / pc4:~# tcpdump: listening on eth0, link-type EN10MB (Ethernet), capture size 65535 bytes / jobs / [1]+ Running tcpdump -s 0 -w /hostlab/pc4.cap & / pc4:~#

hacemos ping de pc1 a pc4
pc1:~# ping -c 3 pc4 / PING pc4 (10.0.0.3) 56(84) bytes of data. / 64 bytes from pc4 (10.0.0.3): icmp_seq=1 ttl=64 time=10.6 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=2 ttl=64 time=0.494 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=3 ttl=64 time=0.365 ms / --- pc4 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2003ms / rtt min/avg/max/mdev = 0.365/3.850/10.693/4.839 ms / pc1:~#

detenemos la captura
r1:~# fg 1 / tcpdump -s 0 -w /hostlab/r1.cap / 1 packets captured / 1 packets received by filter / 0 packets dropped by kernel / r1:~#
pc1:~# fg 1 / tcpdump -s 0 -w /hostlab/pc1.cap / 10 packets captured / 10 packets received by filter / 0 packets dropped by kernel / pc1:~#
pc4:~# fg 1 / tcpdump -s 0 -w /hostlab/pc4.cap / 10 packets captured / 10 packets received by filter / 0 packets dropped by kernel / pc4:~#

wireshark r1

wireshark pc2

wireshark pc4

Como los switches tienen configuradas las redes virtuales y mediante el protocolo de trunking envian los paquetes de las diferentes redes entres switches. pc1 y pc4 están en la misma red, r1 solo recibe el mensaje de broadcast (arp request por broadcast) de pc1 cuando hace ping a pc4, y luego pc1 y pc4 reciben los mensajes de arp request, replay y los icmp de ping. pc2 no recibe nada por que las vlans crean segmentos de broadcast separados para cada red aunque las computadoras están conectadas al mismo switch.
limpiamos las caches
pc2:~# ip -s -s neigh flush all / Nothing to flush. / pc2:~#
pc3:~# ip -s -s neigh flush all / Nothing to flush. / pc3:~#
r1:~# ip -s -s neigh flush all / Nothing to flush. / r1:~#

luego comenzamos el monitores en segundo plano
r1:~# tcpdump -s 0 -w /hostlab/r1.cap / tcpdump: WARNING: eth0: no IPv4 address assigned / tcpdump: listening on eth0, link-type EN10MB (Ethernet), capture size 65535 bytes

hacemos los ping de pc2 a pc3
pc2:~# ping -c 3 pc3 / PING pc3 (192.168.0.3) 56(84) bytes of data. / 64 bytes from pc3 (192.168.0.3): icmp_seq=1 ttl=64 time=10.5 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=2 ttl=64 time=1.49 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=3 ttl=64 time=1.00 ms / --- pc3 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 1998ms / rtt min/avg/max/mdev = 1.007/4.333/10.504/4.368 ms / pc2:~#

lo que observamos en r1 es

pasa algo similar al punto anterior, y el r1 solo recibe el mensaje broadcast inicial cuando se quiere conocer la mac de pc3.

pc1:~# traceroute pc4 / traceroute to pc4 (10.0.0.3), 64 hops max, 40 byte packets / 1 pc4 (10.0.0.3) 11 ms 0 ms 0 ms / pc1:~#

Como pc1 y pc4 están en la misma vlan pueden comunicarse entre si, si bien están en diferentes switches estos usan el protocolo de trunking para poder enviar los paquetes entre computadoras de una misma red en otros switches. Para las computadoras están en la misma red fisica.
pc1:~# traceroute pc3 / traceroute to pc3 (192.168.0.3), 64 hops max, 40 byte packets / 1 r1 (10.0.0.1) 11 ms 0 ms 0 ms / 2 pc3 (192.168.0.3) 4 ms 0 ms 0 ms / pc1:~#

En esta caso siempre es necesario un router para conectar dos vlans (un que esten en el mismo switch). Por lo que el router va a redirigir los mensajes entre computadoras de diferentes redes.
s1:~# brctl show / bridge name bridge id STP enabled interfaces / vlan10 8000.000000000100 no eth0.10 / eth1 / eth3.10 / vlan20 8000.000000000100 no eth0.20 / eth2 / eth3.20 / s1:~#
s2:~# brctl show / bridge name bridge id STP enabled interfaces / vlan10 8000.000000000200 no eth0.10 / eth1 / vlan20 8000.000000000200 no eth0.20 / eth2 / s2:~#

 Tienen el nombre de vlan10 y vlan20. Esta configuración se replica en los dos switches ademas de la configuración para poder hacer trunking entre los dos.
pc1:~# ping -c 3 pc2 / PING pc2 (192.168.0.2) 56(84) bytes of data. / 64 bytes from pc2 (192.168.0.2): icmp_seq=1 ttl=63 time=14.1 ms / 64 bytes from pc2 (192.168.0.2): icmp_seq=2 ttl=63 time=2.04 ms / 64 bytes from pc2 (192.168.0.2): icmp_seq=3 ttl=63 time=1.53 ms / --- pc2 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2002ms / rtt min/avg/max/mdev = 1.534/5.912/14.162/5.837 ms / pc1:~# ping -c 3 pc3 / PING pc3 (192.168.0.3) 56(84) bytes of data. / 64 bytes from pc3 (192.168.0.3): icmp_seq=1 ttl=63 time=2.76 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=2 ttl=63 time=2.46 ms / 64 bytes from pc3 (192.168.0.3): icmp_seq=3 ttl=63 time=1.81 ms / --- pc3 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 2010ms / rtt min/avg/max/mdev = 1.814/2.348/2.764/0.400 ms / pc1:~# ping -c 3 pc4 / PING pc4 (10.0.0.3) 56(84) bytes of data. / 64 bytes from pc4 (10.0.0.3): icmp_seq=1 ttl=64 time=10.6 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=2 ttl=64 time=0.596 ms / 64 bytes from pc4 (10.0.0.3): icmp_seq=3 ttl=64 time=0.718 ms / --- pc4 ping statistics --- / 3 packets transmitted, 3 received, 0% packet loss, time 1998ms / rtt min/avg/max/mdev = 0.596/3.984/10.640/4.706 ms / pc1:~#

 * en este punto no entiendo que cambiaría cuando se hacen los ping.

s1:~# brctl showstp vlan10 / vlan10 / bridge id 8000.000000000100 / designated root 8000.000000000100 / root port 0 path cost 0 / max age 20.00 bridge max age 20.00 / hello time 2.00 bridge hello time 2.00 / forward delay 15.00 bridge forward delay 15.00 / ageing time 300.00 / hello timer 1.03 tcn timer 0.00 / topology change timer 0.00 gc timer 12.03 / flags / eth0.10 (1) / port id 8001 state forwarding / designated root 8000.000000000100 path cost 100 / designated bridge 8000.000000000100 message age timer 0.00 / designated port 8001 forward delay timer 0.00 / designated cost 0 hold timer 0.03 / flags / eth1 (2) / port id 8002 state forwarding / designated root 8000.000000000100 path cost 100 / designated bridge 8000.000000000100 message age timer 0.00 / designated port 8002 forward delay timer 0.00 / designated cost 0 hold timer 0.03 / flags / eth3.10 (3) / port id 8003 state forwarding / designated root 8000.000000000100 path cost 100 / designated bridge 8000.000000000100 message age timer 0.00 / designated port 8003 forward delay timer 0.00 / designated cost 0 hold timer 0.03 / flags / s1:~# brctl showstp vlan20 / vlan20 / bridge id 8000.000000000100 / designated root 8000.000000000100 / root port 0 path cost 0 / max age 20.00 bridge max age 20.00 / hello time 2.00 bridge hello time 2.00 / forward delay 15.00 bridge forward delay 15.00 / ageing time 300.00 / hello timer 1.90 tcn timer 0.00 / topology change timer 0.00 gc timer 3.90 / flags / eth0.20 (1) / port id 8001 state forwarding / designated root 8000.000000000100 path cost 100 / designated bridge 8000.000000000100 message age timer 0.00 / designated port 8001 forward delay timer 0.00 / designated cost 0 hold timer 0.90 / flags / eth2 (2) / port id 8002 state forwarding / designated root 8000.000000000100 path cost 100 / designated bridge 8000.000000000100 message age timer 0.00 / designated port 8002 forward delay timer 0.00 / designated cost 0 hold timer 0.90 / flags / eth3.20 (3) / port id 8003 state forwarding / designated root 8000.000000000100 path cost 100 / designated bridge 8000.000000000100 message age timer 0.00 / designated port 8003 forward delay timer 0.00 / designated cost 0 hold timer 0.90 / flags / s1:~# brctl showmacs vlan10 / port no mac addr is local? ageing timer / 1 00:00:00:00:01:00 yes 0.00 / 2 00:00:00:00:01:01 yes 0.00 / 3 00:00:00:00:01:03 yes 0.00 / s1:~# brctl showmacs vlan20 / port no mac addr is local? ageing timer / 1 00:00:00:00:01:00 yes 0.00 / 2 00:00:00:00:01:02 yes 0.00 / 3 00:00:00:00:01:03 yes 0.00 / s1:~#
s2:~# brctl showstp vlan10 / vlan10 / bridge id 8000.000000000200 / designated root 8000.000000000200 / root port 0 path cost 0 / max age 20.00 bridge max age 20.00 / hello time 2.00 bridge hello time 2.00 / forward delay 15.00 bridge forward delay 15.00 / ageing time 300.00 / hello timer 1.47 tcn timer 0.00 / topology change timer 0.00 gc timer 15.47 / flags / eth0.10 (1) / port id 8001 state forwarding / designated root 8000.000000000200 path cost 100 / designated bridge 8000.000000000200 message age timer 0.00 / designated port 8001 forward delay timer 0.00 / designated cost 0 hold timer 0.47 / flags / eth1 (2) / port id 8002 state forwarding / designated root 8000.000000000200 path cost 100 / designated bridge 8000.000000000200 message age timer 0.00 / designated port 8002 forward delay timer 0.00 / designated cost 0 hold timer 0.47 / flags / s2:~# brctl showstp vlan20 / vlan20 / bridge id 8000.000000000200 / designated root 8000.000000000200 / root port 0 path cost 0 / max age 20.00 bridge max age 20.00 / hello time 2.00 bridge hello time 2.00 / forward delay 15.00 bridge forward delay 15.00 / ageing time 300.00 / hello timer 0.57 tcn timer 0.00 / topology change timer 0.00 gc timer 9.57 / flags / eth0.20 (1) / port id 8001 state forwarding / designated root 8000.000000000200 path cost 100 / designated bridge 8000.000000000200 message age timer 0.00 / designated port 8001 forward delay timer 0.00 / designated cost 0 hold timer 0.00 / flags / eth2 (2) / port id 8002 state forwarding / designated root 8000.000000000200 path cost 100 / designated bridge 8000.000000000200 message age timer 0.00 / designated port 8002 forward delay timer 0.00 / designated cost 0 hold timer 0.00 / flags / s2:~# brctl showmacs vlan10 / port no mac addr is local? ageing timer / 1 00:00:00:00:02:00 yes 0.00 / 2 00:00:00:00:02:01 yes 0.00 / s2:~# brctl showmacs vlan20 / port no mac addr is local? ageing timer / 1 00:00:00:00:02:00 yes 0.00 / 2 00:00:00:00:02:02 yes 0.00 / s2:~#

1. las pc tienen la configuración típica de IP-MAC , los switches y el router tienen la configuración para las vlans. Cada switch tiene la configuración de las vlans y que interfaces van a reenviar el trafico hacia el otro switch (trunk), el router define su dirección mac, y se crean las interfaces lógicas vlan sobre eth0.
2. La separación es meramente lógica, ya que tenemos computadoras de ambas redes distribuidas en diferentes switches, pero estos segmentan los broadcast y conmutan lo mensajes entre host (ya que aprenden las mac), Existe una separación logica entre las redes, pero se propagan por los diferentes switches (trunking).